## Slide 1
P54
Multimodal LLM for
Industrial Task Planning
Overall Project Progress — Sprint 1 to Sprint 5
Computing Technology Project B
Minh · Lakshit · Ved · Dinith · Kaveesha

## Slide 2
Project Overview
OUR GOAL
Build a system that can understand a natural-language robot task, observe the workspace, create an action plan and execute it.
1
LLM converts user instructions into structured commands.
2
Computer vision identifies objects in the workspace.
3
The task planner converts the instruction into robot actions.
4
The executor sends those actions to the simulation robot.
Instruction
→
Vision
→
Planning
→
Robot Execution
2

## Slide 3
The Team
Five members, each owning part of the pipeline
MD
Minh Hoang Duong
Simulation backend architecture, integration and visualisation
LB
Lakshit Bansal
Execution layer, robot integration and simulation design
VM
Ved Jay Makhijani
LLM parser, task planning and evaluation lead
DT
Dinith Thejana
Vision pipeline, YOLO fine-tuning and scene integration
KD
Kaveesha Dulanjana
QA, regression testing, planner safety and documentation
3

## Slide 4
Current System
User
Instruction
→
LLM
Parser
→
YOLO
Vision
→
Task
Planner
→
Executor
→
KUKA /
PyBullet
What it can currently do
Parse structured pick/place/move instructions
Detect and represent workspace objects in simulation
Generate basic action plans such as LOCATE → MOVE → PICK → MOVE → PLACE
Execute pick-and-place tasks using MockRobot or the KUKA simulation controller
Reject some invalid instructions and stop when execution reports a failure
LLM in, rules out
The LLM only handles language. It turns a free-form instruction into a validated command — action, object, destination, confidence.
Everything after that is deterministic: a rule-based planner expands the command into a fixed LOCATE → MOVE → PICK → MOVE → PLACE sequence. The same instruction always produces the same plan, and low-confidence instructions are rejected before the robot moves.
11

## Slide 5
How Far We Have Come
1
Sprint 1
LLM parser, structured instructions and early PyBullet/vision prototype
2
Sprint 2
Task planner, MockRobot, executor and connected pipeline
3
Sprint 3
Spatial planning, multi-step planning API and broader testing
4
Sprint 4
KUKA simulation, configurable workspace and fine-tuned YOLOv8
5
Sprint 5
Qwen/Ollama, response cache, Docker work and ROS2 preparation
5

## Slide 6
Sprint 1
Foundations — instruction parser and simulation prototype
LLM parser built
Structured instruction schema, prompt design and edge-case handling, tested without API calls.
Model selected
GPT-4o, Gemini and DeepSeek compared over 25 instructions; GPT-4o chosen on accuracy and latency.
Vision approach chosen
YOLOv8 with OpenCV selected as the hybrid detector, plus a scene format for the planner.
Simulation prototype
PyBullet workspace built from scratch: KUKA arm, coloured blocks, camera and colour detection.
6

## Slide 7
Sprint 2
Task planning, execution and the connected pipeline
Rule-based task planner
Four action types, each decomposed into a fixed, deterministic sequence of robot primitives.
Robot command schema
A shared command contract between planner and executor, validated at the boundary.
MockRobot and executor
A stateful stand-in robot with per-command timeouts and graceful failure handling.
Pipeline connected
All five stages wired together end to end, with vision stubbed until Sprint 3.
7

## Slide 8
Sprint 3
Spatial reasoning, evaluation baseline and real execution
Spatial language handled
Eight relations such as left of, near and on top of resolved into workspace offsets.
Multi-step planning
Several parsed instructions combined into a single renumbered action plan.
Baseline parser
A zero-LLM keyword matcher built as the control group for measuring what the LLM adds.
Real robot execution
PyBullet inverse kinematics and grasping: the first full pick-and-place end to end.
8

## Slide 9
Sprint 4
Beta stabilisation, fine-tuned vision and report integrity
Fine-tuned YOLOv8n
Trained on a synthetic PyBullet dataset covering seven workspace classes.
KUKA execution path
Full LOCATE → MOVE → PICK → MOVE → PLACE runs completed on the KUKA IIWA in simulation.
Evaluation expanded
Test set grown from 25 to 35 instructions, with end-to-end parse latency benchmarked.
Consistency audit
Reported figures re-derived from committed code and data; the known safety gap logged openly.
9

## Slide 10
Sprint 5
Local LLM, packaging and multi-action instructions
Local LLM backend
Qwen 2.5 through Ollama, giving an offline option for privacy-sensitive deployment.
Response cache
Repeated instructions served from disk instead of the API — 107 s down to 4 ms.
Docker packaging
Ollama and the pipeline run as containers, with a ROS2/MoveIt image prepared.
Multi-action commands
One instruction can now carry several actions, planned and executed in order.
10

## Slide 11
Key Progress So Far
Fine-tuned YOLOv8n for 7 workspace classes.
KUKA/PyBullet pick-and-place implementation and recorded successful simulation execution.
Qwen 2.5 integrated through Ollama for local LLM processing.
Persistent response cache added to speed up repeated instructions.
Docker configurations and ROS2/UR5 integration scaffold prepared.
General multi-action command integration.
12

## Slide 12
Into the Physical World
Induction completed at the Factory of the Future (FOF) lab
Workspace bins and overhead sensors
Component trays and part fixtures
Assembly pick fixtures
The physical UR robot arm
Robot, controller and workspace
Introduced to the physical arm, its controller and the assembly cell we will deploy into.
A real workspace, not a simulated one
Labelled bins, component trays and printed fixtures replace the simulated blocks and trays.
13

## Slide 13
Next Steps
1
Physical cameras
Mount and calibrate real cameras over the FOF workspace.
2
Re-finetune YOLOv8
Retrain on the physical parts, bins and lighting of the real cell.
3
Rewrite detection maths
Inverse kinematics and camera-to-robot coordinates currently assume PyBullet.
4
Rewrite robot controller
Drive the real arm through the robot controller, reached over TCP via the PLC.
5
Spatial command execution
Improve spatial handling against the real workspace geometry.
6
Final integration and testing
Complete end-to-end testing on the physical system.
Thank You!!!